## Slide 1
CPE126-4 · Introduction to Artificial Intelligence · Mapúa University
Vehicle Classification
for Adaptive Traffic
Control Systems
Using CNNs
Gilbert E. Solis
Mapúa University · March 2026
TensorFlow / Keras · MobileNetV2 · Transfer Learning · MIO-TCD Dataset

## Slide 2
Problem Statement & Objectives
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
2 / 12
Problem Statement
Current traffic management systems rely on static timers or basic inductive sensors that cannot adapt to real-time road conditions.
There is a growing need for an accessible, vision-based vehicle classification system capable of accurately identifying different vehicle classes from low-resolution CCTV traffic camera imagery.
This system serves as a foundational component for dynamic, AI-driven adaptive traffic flow analysis and intelligent infrastructure management.
Project Objectives
01
Load & Explore Dataset
Collect and analyze the MIO-TCD labeled dataset (~52,800 images, 11 vehicle classes)
02
Preprocess & Augment
Normalize, resize, and augment image data to prevent overfitting during training
03
Build & Train CNN
Implement MobileNetV2 transfer learning with two-stage frozen + fine-tune training
04
Evaluate Performance
Assess accuracy, precision, recall, F1-score, and analyze the confusion matrix
05
Validate Real-World Use
Test on unseen CCTV images using the inference demo to confirm applicability

## Slide 3
Dataset Overview — MIO-TCD
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
3 / 12
~52,800
Total Images
11
Vehicle Classes
128×128
Training Resolution
4.2×
Max Class Imbalance
⚠ Key Dataset Challenges
• Low-resolution CCTV crops — limited texture detail • Class imbalance: background (7,296) vs non-motorized (1,751) • Visual similarity — trucks, vans, pickups share silhouettes • Illumination variation — day / night CCTV footage
Chart: Images per Class
| art.truck | background | bicycle | bus | car | motorcycle | non-motor. | pedestrian | pickup.trk | su.truck | work.van
Images | 4991 | 7296 | 2284 | 5102 | 6268 | 1982 | 1751 | 6262 | 6290 | 5120 | 5455

## Slide 4
Methodology — End-to-End CNN Pipeline
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
4 / 12
01
RAW DATA
MIO-TCD
52,800 images
11 classes
02
AUGMENT
Flip · Rotate
Zoom · Translate
Contrast
03
MobileNetV2
Pretrained
ImageNet
Weights
04
CLASS HEAD
GAP → Drop
→ Dense(11)
Softmax
05
PREDICTION
11-Class
Vehicle
Label
Two-Stage Training Strategy
STAGE 1 — Frozen Backbone | LR = 1e-3 | Train classification head only
STAGE 2 — Partial Fine-Tuning | LR = 1e-5 | Last 30 backbone layers unfrozen

## Slide 5
Two-Stage Training Strategy
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
5 / 12
STAGE 1 — Frozen Backbone
Backbone
MobileNetV2 — ALL layers FROZEN
Head
GAP → Dropout(0.35) → Dense(11, softmax)
Optimizer
Adam | Learning Rate = 1e-3
Loss
Sparse Categorical Crossentropy
Max Epochs
20 (EarlyStopping patience = 6)
Class Weights
Balanced — boosts minority class gradient
Purpose
Stabilize head before touching backbone
Why Freeze?
Prevents random head gradients from corrupting ImageNet features
STAGE 2 — Partial Fine-Tuning
Backbone
Last 30 layers UNFROZEN (fine-tuned)
BatchNorm
training=False — preserves ImageNet BN stats
Optimizer
Adam | Learning Rate = 1e-5 (100× smaller)
Loss
Sparse Categorical Crossentropy
Max Epochs
20 (EarlyStopping patience = 6)
Class Weights
Same balanced weights as Stage 1
Purpose
Adapt high-level features to vehicle imagery
Why Small LR?
Avoids catastrophic forgetting of ImageNet weights

## Slide 6
Anti-Overfitting Techniques
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
6 / 12
Data Augmentation
Random flip, ±14° rotation,
±10% zoom, ±10% translation,
±15% contrast — applied inside
the model (auto-off at inference)
Dropout (35%)
Randomly zeros 35% of
neurons per training step.
Forces redundant feature
learning in the head layer.
L2 Regularization
Weight decay λ = 1e-4
applied to Dense output layer.
Penalizes large weights;
reduces overconfident boundaries.
Class Weights
Balanced weights via sklearn.
Boosts gradient contribution
from minority classes (bicycle,
motorcycle, non-motorized).
EarlyStopping
Monitors val_loss.
Patience = 6 epochs.
Restores best weights
automatically on trigger.
ReduceLROnPlateau
Monitors val_loss.
Halves LR (factor = 0.5)
after 3 plateau epochs.
Min LR floor = 1e-7.

## Slide 7
Training Results — Stage 1 + Stage 2 Combined History
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
7 / 12
Chart: Accuracy per Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
Train Accuracy | 0.58 | 0.65 | 0.66 | 0.67 | 0.67 | 0.67 | 0.67 | 0.67 | 0.68 | 0.69 | 0.69 | 0.68 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.7 | 0.61 | 0.67 | 0.7 | 0.72 | 0.74 | 0.75 | 0.76 | 0.77 | 0.78 | 0.79 | 0.8 | 0.81 | 0.81 | 0.82 | 0.82 | 0.82 | 0.83 | 0.83 | 0.84 | 0.84
Validation Accuracy | 0.69 | 0.7 | 0.71 | 0.72 | 0.72 | 0.72 | 0.7 | 0.71 | 0.71 | 0.73 | 0.7 | 0.74 | 0.7 | 0.73 | 0.73 | 0.72 | 0.73 | 0.73 | 0.73 | 0.74 | 0.76 | 0.77 | 0.78 | 0.79 | 0.8 | 0.81 | 0.81 | 0.82 | 0.82 | 0.83 | 0.83 | 0.84 | 0.84 | 0.84 | 0.85 | 0.85 | 0.85 | 0.85
Chart: Loss per Epoch
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38
Train Loss | 1.31 | 1.06 | 1.05 | 1.02 | 1.04 | 1.035 | 1.03 | 1.02 | 1.01 | 0.98 | 0.955 | 0.95 | 0.948 | 0.942 | 0.95 | 0.92 | 0.91 | 0.9 | 1.32 | 1.01 | 0.91 | 0.84 | 0.8 | 0.76 | 0.72 | 0.69 | 0.66 | 0.63 | 0.605 | 0.585 | 0.575 | 0.545 | 0.53 | 0.52 | 0.495 | 0.485 | 0.478 | 0.462
Validation Loss | 0.9 | 0.86 | 0.84 | 0.82 | 0.82 | 0.83 | 0.86 | 0.87 | 0.82 | 0.79 | 0.87 | 0.77 | 0.85 | 0.77 | 0.8 | 0.8 | 0.8 | 0.8 | 0.84 | 0.75 | 0.71 | 0.67 | 0.64 | 0.61 | 0.58 | 0.56 | 0.54 | 0.53 | 0.52 | 0.505 | 0.495 | 0.49 | 0.475 | 0.47 | 0.46 | 0.455 | 0.45 | 0.435
Stage 1 (Epochs 1–18, frozen): Head-only training. Val accuracy rises and plateaus at ~73%. Stage 2 (Epochs 18–38, fine-tune): Last 30 layers unfrozen at LR=1e-5. After an initial "spike" in loss at Epoch 19 (due to weight updates), Val accuracy climbs steadily to ~85%.

## Slide 8
Model Evaluation — Test Set Results
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
8 / 12
85.46%
Test Accuracy
0.8365
Macro F1-Score
0.8425
Macro Recall
0.8355
Macro Precision
Per-Class Performance Report
Class | Prec. | Recall | F1 | Support | Notes
articulated_truck | 0.7337 | 0.8278 | 0.7779 | 749 | Long profile; distinct shape
background | 0.9780 | 0.9352 | 0.9561 | 1,095 | No vehicle, easy to distinguish
bicycle | 0.8280 | 0.8280 | 0.8280 | 343 | Low-res confusion with motorcycle
bus | 0.9229 | 0.9229 | 0.9229 | 765 | Large, distinctive silhouette
car | 0.9168 | 0.8787 | 0.8973 | 940 | Most common class; stable
motorcycle | 0.8972 | 0.8519 | 0.8739 | 297 | Smallest non-rare class; bicycle overlap
non-motorized_veh. | 0.5376 | 0.7605 | 0.6299 | 263 | Rarest class; hardest to classify
pedestrian | 0.9186 | 0.9010 | 0.9097 | 939 | Upright figure; mostly distinct
pickup_truck | 0.8445 | 0.8919 | 0.8676 | 944 | Confused with work_van
single_unit_truck | 0.7342 | 0.6940 | 0.7135 | 768 | Confused with articulated_truck
work_van | 0.8795 | 0.7763 | 0.8247 | 818 | Boxy shape overlaps trucks

## Slide 9
Inference Demo — Real-World CCTV Classification
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
9 / 12
Saved model loaded in inference_demo.ipynb — randomly selects 5 unseen CCTV images and classifies them without any retraining.
📷
CCTV
Image
background
99.9%
HIGH confidence
#2 single_unit_truck 2.1%
📷
CCTV
Image
car
72.5%
HIGH confidence
#2 pickup_truck 4.3%
📷
CCTV
Image
work van
46.2%
MED confidence
#2 single_unit_truck 14.2%
📷
CCTV
Image
pedestrian
99.9%
HIGH confidence
#2 bicycle 6.8%
📷
CCTV
Image
car
66.5%
MED confidence
#2 pickup_truck 18.5%
inference_demo.ipynb — Loads saved model · Scans test folder · Selects N random images · Preprocesses to 128×128 · Returns Top-3 per image Re-run a single cell for a completely new batch — no kernel restart, no retraining needed.

## Slide 10
Generalization Analysis — Overfitting / Underfitting Diagnosis
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
10 / 12
Chart: Train vs. Validation vs. Test Accuracy
| Train Acc (at best val epoch) | Best Validation Acc | Test Acc (held-out)
Accuracy (%) | 84.29 | 85.2 | 85.46
Train–Val gap: ~0.92% (threshold < 10%)
✓ WELL-GENERALIZED
Train–Val gap of ~0.92% is within healthy range.
Test accuracy (85.46%) is consistent with validation (84.29%).
Model generalizes reliably to unseen CCTV images.
What Drove Generalization
Two-stage training — stable convergence, no catastrophic forgetting
Class weights — improved recall on bicycle, motorcycle, non-motorized
Mild CCTV-realistic augmentation — generalized without underfitting
Dropout + L2 regularization — prevented head overfitting
EarlyStopping — locked in the best generalization checkpoint

## Slide 11
Conclusion & Future Improvements
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
11 / 12
Key Conclusions
Test Accuracy:
85.46% on completely held-out MIO-TCD test set
Macro F1:
0.8365 — strong performance across all 11 classes
Backbone:
MobileNetV2 + ImageNet: fast, stable convergence
Two-Stage:
Prevented catastrophic forgetting; clean curves
Hardest pair:
single unit truck ↔ articulated truck at CCTV low resolution
Gap analysis:
0.92% train–val gap — no significant overfitting
Future Improvements
Larger Input:
160×192 px — may recover lost fine detail
TTA:
Test-Time Augmentation for marginal accuracy gain
Ensemble:
Two MobileNetV2 models on different random seeds
Label Smooth:
smoothing=0.1 reduces overconfident predictions
Grad-CAM:
Visualize what the model attends to per image
TFLite Deploy:
Convert to .tflite for edge / Raspberry Pi deployment

## Slide 12
References
Vehicle Classification for Adaptive Traffic Control · CPE126-4 · Mapúa University
12 / 12
[1]
Luo, Z. et al. (2018). MIO-TCD: A new benchmark dataset for vehicle classification and localization. IEEE Transactions on Image Processing, 27(10), 5129–5141.
[2]
Sandler, M. et al. (2018). MobileNetV2: Inverted residuals and linear bottlenecks. Proceedings of the IEEE CVPR 2018.
[3]
Yosinski, J. et al. (2014). How transferable are features in deep neural networks? Advances in Neural Information Processing Systems, 27.
[4]
TensorFlow. (2024). Transfer learning and fine-tuning guide. https://www.tensorflow.org/tutorials/images/transfer_learning
[5]
Chollet, F. (2021). Deep Learning with Python, 2nd Edition. Manning Publications.
[6]
Kaggle Dataset — MIO-TCD 50,000 Images Classification. https://www.kaggle.com/datasets/yash88600/miotcd-dataset-50000-imagesclassification
[7]
Scikit-learn. (2024). compute_class_weight. https://scikit-learn.org/stable/modules/generated/sklearn.utils.class_weight.compute_class_weight.html